## Slide 1: PCBA Allocation Ranking Logic and Allocation Procedures
Ken Wang
Nov, 2020

## Slide 2: Key Objectives for Allocation Tool
Productivity: reduce the weekly x hours manual efforts for each BU to a few minutes total effort
Consistency: ensure an agreed allocation logic based on priority and urgency for all BU which aligns with central guidance and DF operations
Fairness: consider transit time for remote DF in allocation

## Slide 3: Core Allocation Concept
First, rank orders globally
Then, allocate supply to each order per the ranking.

## Slide 4: Order Ranking Logic
Top priority orders
(PR1/2/3, Top100, L4, BUP)
Order qty
Additional considerations:
Deprioritize MFG hold orders – put behind all other orders
DPAS: some under PR7/8 instead of PR1/2/3, recategozied as PR1
Prioritize Aged and recommited
OSSD
Current FCD
Prioritize earlier FCD
Prioritize rev order
Priority number:
PR1: 1
PR2: 2
PR3: 3
Top100: 4
L4: 5
BUP: 6
Rev/non-rev
Prioritize smaller qty order
(date offset by PCBA to DF transit time)
Logic discussed and aligned with all DF managers; PPF team alignment in progress.
Manual exceptional priority injection by PSP
Note:
Minor change on the logic to put order qty ahead of rev/non-rev compare with initial version reviewed with DF managers
We will continue to review if different logic should be put in for different situation (e.g. qend, or even different BU if we should)

## Slide 5: PCBA Allocation – Input Data and Porcedures
GLO 3A4
SCR
DF Site OH
DF Site Intransit
Ranking GLO 3A4
OH allocate to Site 3A4
Intransit allocate to Site 3A4
SCR allocate to GLO 3A4
SCR allocation result
Input Data
Main procedures
Transit time
Versions: different versions considered as same
Sourcing rules: each DF only source same TAN from one PCBA site
Transit time: air transit time – backlog gap should be covered by air ship
Assumptions:
ETA<=15days considered as OH; ETA>15days can backward fulfill -10 days OSSD
Offsset 3A4 OSSD, FCD
Other exceptional data considered:
Exceptional priority
cross-CM intransit
TAN grouping

## Slide 6: Solution Diagram
3A4 Backlog
(UOV)
Exceptional priority, TAN grouping, Cross CM intransit
(Smartsheet)
Cisco IT Cloud
(http://pcba-allocation.cisco.com:5000/allocation)
Web UI
Allocation App
Storage
Port:37600
OH, in-transit, SCR
(MongoDB: SCDx)

## Slide 7: Transit Time
PCBA Site | DF Site | Transit Time (days)
FOL | FTX | 7
 | FCZ | 9
 | FJZ | 10
 | SJZ | 10
 | JMX | 9
 | FGU | 9
 | JPE | 4
 | JPI | 5
 | FSJ | 6
 | FVE | 9
 | SHK | 2
 | FDO | 4
 | FOC | 1
 | Other | 7

## Slide 8: Manual SS Priority Injection
User can flag and give a new priority rank for any SS when need to (for existing priority orders will replace with new ranking# provided) – we should only use this very exceptionally so as not to deviate too much from the normal priority process.
How:
Add the SS into smartsheet via: https://app.smartsheet.com/sheets/vMWf8q5CPR24P52rCpxMx6H5gcv3Hx4Q3mF82pG1?view=grid
Give a specific ranking# to the SS. Example:
  1 – make the order same priority as PR1;
  1.5 - make the order lower than PR1 but higher than PR2;
  or any number >6 - make the order lower than BUP, but higher than any other order

## Slide 9: Note
Current design applies to orgs have different name between PCBA and DF.
If for same org code case, e.g. FDO, need to have a way to distinguish OH for DF vs PCBA; also currently pcba_site is removed from OH data so DF OH will also get removed, thus this need to be modified.